## Slide 1
MY STUDY NOTES
Building a Poroelasticity Solver in Rust
Theory, numerical methods, the full workflow, and a block-by-block walkthrough of every
file in the project — written so I can explain any part of this to my professor.
Projects covered:
F:\rust\poroelastic_solver (the main Rust crate)
F:\rust\wang2003 (Rung 0 learning project)
F:\rust\POEL_2024-main (reference Fortran code, compiled & run, not written by me)

## Slide 2
PART 1
Theory
What poroelasticity is, the governing equations, the five parameters, and the boundary conditions.

## Slide 3
PART 1 · THEORY
What Is Poroelasticity?
Rock underground is not solid — it's a porous skeleton with fluid (water) filling the pore space.
Two things can happen when you inject fluid: (1) pore pressure rises, and (2) the rock skeleton deforms.
The key idea of poroelasticity: these two effects are coupled, not independent.
  Squeezing the rock (deformation) changes the pore pressure. Raising the pore pressure pushes the rock apart (deformation). You cannot solve one without the other.
This is exactly the physics behind injection-induced earthquakes (the PNAS paper's subject): wastewater injection raises pressure, which reduces the effective stress holding a fault locked, which can trigger slip.

## Slide 4
PART 1 · THEORY
The Governing Equations
Zhai et al. (2019) Eqs. 1-2 == Wang & Kumpel (2003) Eqs. 1-2
Eq. 1 (momentum balance / quasi-static elasticity):
G*Laplacian(u) + G/(1-2*nu)*grad(div(u)) - alpha*grad(p) = f(x,t)
Eq. 2 (pore-pressure diffusion, coupled to strain rate):
(1/Q)*dp/dt + alpha*d(div(u))/dt - div(chi*grad(p)) = q(x,t)
u(x,t) — displacement vector (how much the rock moves). p(x,t) — excess pore pressure.
Eq. 1 says: elastic restoring forces (Laplacian + grad-div terms) balance the pressure gradient's push (alpha*grad(p)).
Eq. 2 says: pressure changes (dp/dt) come from two sources — fluid diffusing in (div(chi*grad p)) and the rock's own volume changing (d(div u)/dt) — the coupling term.
Setting alpha=0 decouples them into ordinary elasticity + ordinary diffusion; the physics of interest is entirely in the alpha terms.

## Slide 5
PART 1 · THEORY
The Five Independent Parameters
Symbol | Name | Meaning
G | Shear modulus | Stiffness against shape change (Pa)
ν | Drained Poisson ratio | Elastic response when fluid can freely escape
νᵤ | Undrained Poisson ratio | Elastic response when fluid is trapped (νᵤ > ν always)
B | Skempton coefficient | Pore-pressure rise per unit confining-pressure rise, undrained
D | Hydraulic diffusivity | How fast pressure disturbances spread (m²/s)
Everything else (α, Q, χ, λ) is computed from these five — see the next slide.

## Slide 6
PART 1 · THEORY
Deriving the Coupling Constants
Wang & Kumpel (2003), Eqs. 3-6 -- implemented verbatim in src/param.rs
lambda = 2*nu*G / (1 - 2*nu) (Eq. 3)
alpha = 3*(nu_u - nu) / [(1-2*nu)*(1+nu_u)*B] (Eq. 4)
1/Q = (9/2)*(1-2*nu_u)*(nu_u-nu) / [(1-2*nu)*(1+nu_u)^2*G*B^2] (Eq. 5)
chi = (9/2)*(1-nu_u)*(nu_u-nu)*D / [(1-nu)*(1+nu_u)^2*G*B^2] (Eq. 6)
lambda — the first Lame parameter; ordinary elasticity, no fluid coupling at all.
alpha (Biot-Willis coefficient) — fraction of a pore-pressure change that shows up as effective stress. Close to 1 means very strong coupling.
Q (Biot modulus) — how much pressure builds up per unit of fluid volume added at constant strain (a stiffness for the fluid+pore system).
chi (mobility = permeability / viscosity) — NOT the same as D! D = chi * Q. Units are m^2/(Pa*s), not m^2/s.

## Slide 7
PART 1 · THEORY
Boundary Conditions: Approximating a Half-Space
z = 0 (the ground surface, free surface):
  Traction-free: sigma_xz = sigma_yz = sigma_zz = 0 (nothing is pushing on the surface from above)
  Drained: p = 0 (pressure equilibrates instantly with the atmosphere)
All other faces (far-field, the domain's necessary truncation of an infinite half-space):
  Fixed zero displacement (rock far away doesn't move)
  No-flow / zero pressure gradient (no fluid crosses the boundary)
Caveat: domain must be much larger than the diffusion length sqrt(D*t) reached during a run, or these truncation boundaries contaminate the answer — this is exactly what we saw happen at late times in the validation.

## Slide 8
PART 1 · THEORY
Two Ways to Solve the Same Equations
THE PAPER'S WAY (semi-analytical)
Laplace transform removes time (t -> s)
Hankel transform removes radius (r -> k, wavenumber)
Left with an ODE in depth z only -> solve with Haskell's propagator matrix
Numerically invert both transforms to get back to (r, z, t)
Exact for axisymmetric point sources in layered media; POEL2024 implements this
OUR WAY (direct numerical)
No transforms at all -- discretize x, y, z, and t directly
Finite differences on a uniform 3D grid
Backward Euler in time (unconditionally stable)
Iterate elasticity <-> diffusion each time step until pressure stops changing
Simpler to implement and reason about; costs more compute, needs a large domain

## Slide 9
PART 2
Our Numerical Method
How the finite-difference discretization, linear solvers, and coupling scheme actually work.

## Slide 10
PART 2 · NUMERICAL METHOD
Overview: Grid, Time, Iteration
Grid: a uniform structured 3D grid (Grid3D). Nodes at (i,j,k), physical position (i*dx, j*dy, k*dz). z increases with depth.
Every field (pressure, each displacement component) is a flat Vec<f64> the same length as the grid, indexed via idx(i,j,k) = i + nx*(j + ny*k).
Time stepping: backward Euler -- fully implicit, so any time step size dt is numerically stable (though large dt loses temporal accuracy).
Each time step is NOT a single linear solve: elasticity and diffusion are coupled equations, so we iterate between the two (an 'outer' or 'Picard-type' loop) until they agree.

## Slide 11
PART 2 · NUMERICAL METHOD
Discretizing the Elasticity Equation
Expanding G*Laplacian(u) + (lambda+G)*grad(div(u)) for the x-component gives:
Same pattern (cyclically) for Ly, Lz
Lx = (lambda+2G)*d2ux/dx2 + G*d2ux/dy2 + G*d2ux/dz2
+ (lambda+G)*d2uy/dxdy + (lambda+G)*d2uz/dxdz
Every second derivative uses standard central differences: d2f/dx2 = (f[i+1] - 2f[i] + f[i-1]) / dx^2
Cross derivatives (like d2uy/dxdy) need a 4-point stencil: (f[i+1,j+1] - f[i+1,j-1] - f[i-1,j+1] + f[i-1,j-1]) / (4*dx*dy)
This couples all three displacement components together at every interior grid point -- that's why elasticity alone is a 3*N unknown linear system (N = number of grid nodes).

## Slide 12
PART 2 · NUMERICAL METHOD
The Free-Surface Trick: Ghost Nodes
The stencil at the surface (k=0) needs a neighbor 'above the surface' (k=-1) that doesn't physically exist.
Solution: invent a 'ghost' value at k=-1, chosen so the traction-free condition is satisfied exactly.
elasticity.rs :: ghost_ux / ghost_uy / ghost_uz
// sigma_xz = 0 => dux/dz = -duz/dx =>
ux_ghost(k=-1) = ux(k=1) + 2*dz * duz_dx
// sigma_zz = 0 (and p=0 at surface) => duz/dz = -lambda/(lambda+2G) * (dux_dx+duy_dy) =>
uz_ghost(k=-1) = uz(k=1) + 2*dz * (lambda/(lambda+2G)) * (dux_dx + duy_dy)
At the lateral edges (i=0, i=nx-1, j=0, j=ny-1) the far-field zero-displacement condition takes priority over this formula (returns 0.0) since those columns are pinned anyway.

## Slide 13
PART 2 · NUMERICAL METHOD
Discretizing the Diffusion Equation
diffusion.rs :: apply_diffusion_operator
// backward Euler: solve for p at the NEW time step
(1/(Q*dt)) * p_new - div(chi * grad(p_new)) = source + (1/(Q*dt)) * p_old
// 7-point Laplacian stencil (interior nodes):
lap = chi * [ (p[i+1]-2p[i]+p[i-1])/dx^2 + (...)/dy^2 + (...)/dz^2 ]
z=0 (drained surface): p is fixed at 0 -- not solved for, just held constant.
All other boundaries: no-flow -- implemented by mirroring the neighbor across the boundary node (ghost = value one node further in), giving zero gradient there.
This backward-Euler operator is symmetric positive-definite, which is exactly what conjugate gradient needs.

## Slide 14
PART 2 · NUMERICAL METHOD
Two Different Linear Solvers, On Purpose
Conjugate Gradient (CG)
Used for: the diffusion equation
Requires: the operator to be symmetric positive-definite (SPD)
Why it qualifies: the 7-point stencil + Dirichlet/Neumann boundary treatment is provably symmetric
BiCGSTAB
Used for: the elasticity equation
Requires: nothing in particular -- works for general (non-symmetric) operators
Why it's needed here: the free-surface ghost-node formulas are NOT guaranteed to keep the discrete operator exactly matrix-symmetric
Both are matrix-free: the operator is applied as a stencil function, never assembled into an explicit matrix.

## Slide 15
PART 2 · NUMERICAL METHOD
Coupling, Attempt 1: Plain Iteration (Picard)
Idea: guess a pressure field, solve elasticity for displacement, recompute the strain-rate source this implies, resolve pressure, repeat until pressure stops changing.
This worked for moderate coupling (e.g. alpha=0.385, ~10 iterations to converge).
WHAT WENT WRONG
For Wang & Kumpel's own parameters (alpha=0.95, very soft/strongly-coupled rock), this iteration diverged: pressure went from -1e4 Pa to -7.7e5 Pa in a single additional step.
Not slow convergence -- genuine numerical instability. This is a well-known failure mode for naive iterative coupling of Biot's equations at high alpha.

## Slide 16
PART 2 · NUMERICAL METHOD
Coupling, Attempt 2: Fixed-Stress Split
The fix (Kim, Tchelepi & Juanes 2011; Mikelic & Wheeler 2013): hold TOTAL stress fixed during the pressure solve, using K_dr*epsilon_v = sigma_v + alpha*p to predict how strain must shift:
coupling.rs :: step()
beta = alpha^2 / K_dr // stabilization coefficient, K_dr = drained bulk modulus
// modified flow step (solved FIRST each iteration):
(1/Q + beta)/dt * p_new - div(chi*grad(p_new))
= source + beta/dt * p_prev_iter + (1/Q)/dt * p_start_of_step
Order flips: solve flow first (with the extra beta term), THEN mechanics with the updated pressure.
Provably unconditionally stable regardless of coupling strength -- exactly what was missing.
Result: the same alpha=0.95 case that diverged now runs cleanly and matches POEL2024 to 0.2-2.5% at early times.

## Slide 17
PART 3
The Workflow
What we actually did, in order -- useful for retracing any step or explaining the process.

## Slide 18
PART 3 · WORKFLOW
Step 1 — Parameter Conversion (Rung 0)
📁 F:\rust\wang2003\src\main.rs
Before writing any solver, hand-derived lambda, alpha, 1/Q, chi for Wang & Kumpel's worked example and checked them against the code's output.
Built this as a tiny standalone learning project (wang2003) using plain variables first, no structs -- the simplest possible Rust.
Every number matched the hand calculation exactly: lambda=2.667e8 Pa, alpha=0.952, Q=1.47e9 Pa, chi=1.531e-9 m^2/(Pa*s).
This 'verification ladder' idea (simplest case first, add complexity only after each step is trusted) shaped the entire project.

## Slide 19
PART 3 · WORKFLOW
Step 2 — Core Solver Infrastructure
📁 F:\rust\poroelastic_solver\src\{grid,field,param}.rs
Grid3D: a uniform 3D grid with node indexing, defined once, reused everywhere.
Field3D / VectorField3D: scalar and vector data living on that grid, stored as flat arrays for speed.
PoroLayer: the 5-parameter to lambda/alpha/Q/chi conversion, carried over from the Rung 0 project.
Design choice: keep the crate dependency-free (pure Rust std library) so it builds anywhere without fighting BLAS/LAPACK installs.

## Slide 20
PART 3 · WORKFLOW
Step 3 — Elasticity Solver + First Validation
📁 F:\rust\poroelastic_solver\src\elasticity.rs, tests\elasticity_mms.rs
Wrote the Navier-Cauchy finite-difference stencil, the free-surface ghost-node formulas, and a BiCGSTAB solver.
Validation: Method of Manufactured Solutions (MMS) -- plug a known quadratic displacement field into the stencil and check it reproduces the exact analytic answer.
Why quadratics: central differences are exact (to machine precision) for degree <= 2 polynomials, so this isolates stencil bugs from boundary-condition bugs.
Result: passed to within 1e-8 relative error on the first correct attempt.

## Slide 21
PART 3 · WORKFLOW
Step 4 — Diffusion Solver + Second Validation
📁 F:\rust\poroelastic_solver\src\diffusion.rs, tests\diffusion_point_source.rs
Wrote the backward-Euler pressure diffusion stencil and a conjugate-gradient solver.
Validation: compared against the classical closed-form solution for a continuous point source in an infinite medium (Carslaw & Jaeger).
First attempt used too short a test duration -- compared at a point so far past the diffusion front that the analytical curve's steep tail amplified small errors into a false failure.
Fix: ran longer (t=1200s) so the comparison point sat in a numerically well-behaved part of the curve. Result: 0.2-2.5% error.

## Slide 22
PART 3 · WORKFLOW
Step 5 — Coupling + a Working End-to-End Demo
📁 F:\rust\poroelastic_solver\src\coupling.rs, source.rs, main.rs
Wrote InjectionWell (Gaussian-smoothed point source) and the first coupling loop (plain Picard iteration).
main.rs runs a 60-day constant-rate injection into a homogeneous half-space with moderate crustal parameters (alpha=0.385) -- converges cleanly in ~10 iterations/step.
This became the first fully working demonstration: pore pressure builds up at the well, the ground surface lifts a fraction of a millimeter -- physically sensible end to end.

## Slide 23
PART 3 · WORKFLOW
Step 6 — Bringing In POEL2024 As Ground Truth
📁 F:\rust\POEL_2024-main (Fortran, not written by me)
POEL2024 is Rongjiang Wang's own reference implementation of the Wang & Kumpel (2003) method.
Bug 1: the prebuilt .exe needed MinGW runtime DLLs that weren't installed. Fixed by installing gfortran (via MSYS2 pacman) and compiling from source.
Bug 2: an idealized near-point source (tiny radius) pushed the Hankel-transform wavenumber integration to its array-size cap and segfaulted. Fixed by widening the source to a more realistic (still small) size.
Bug 3: a source that jumped straight to full rate on its first time sample had no frequency content for the transform machinery to resolve, giving all-zero output. Fixed by giving it an explicit onset at t=1s.

## Slide 24
PART 3 · WORKFLOW
Step 7 — Discovering the Picard Divergence
📁 F:\rust\poroelastic_solver\examples\wk2003_comparison.rs
Configured our own Rust solver with Wang & Kumpel's exact test-case parameters (the same ones driving POEL2024) to compare directly.
Pressure diverged: -1.07e4 Pa at t=100s, then -7.77e5 Pa at t=200s -- a ~70x jump in one step.
Diagnosis: not a bug in the stencils (those were already validated) -- the plain Picard coupling iteration is known to be unstable for strongly-coupled media (alpha=0.95, close to the theoretical maximum of 1).

## Slide 25
PART 3 · WORKFLOW
Step 8 — Fixed-Stress Split, Final Result
📁 F:\rust\poroelastic_solver\src\diffusion.rs, coupling.rs
Implemented the fixed-stress split (see Part 2) -- flow solved first each iteration, with the beta=alpha^2/K_dr stabilization term.
Regression check: moderate-coupling case (main.rs) produced byte-identical output to before -- confirms nothing broke.
The strongly-coupled case now runs cleanly through all 80 steps, matching POEL2024 to 0.2-2.5% at early time (later drift traced to finite-domain boundary effects, not the coupling scheme).

## Slide 26
PART 4
Code Walkthrough
Every source file, block by block: what it does, where it lives, and how it works.

## Slide 27
PART 4 · CODE WALKTHROUGH
Project Layout
F:\rust\poroelastic_solver\ <- the main crate
Cargo.toml package manifest, zero dependencies
src\
lib.rs crate root, re-exports public API
grid.rs Grid3D the structured 3D grid
field.rs Field3D/VectorField3D data living on the grid
param.rs PoroLayer the 5-parameter -> alpha/Q/chi conversion
linalg.rs conjugate_gradient, bicgstab matrix-free linear solvers
elasticity.rs apply_elastic_operator, solve_elasticity, divergence
diffusion.rs apply_diffusion_operator, solve_diffusion
coupling.rs SimState, step() the fixed-stress split time loop
source.rs InjectionWell Gaussian-smoothed point source
main.rs example: 60-day injection demo
tests\ elasticity_mms.rs, diffusion_point_source.rs
examples\ plot_diffusion_validation.rs, wk2003_comparison.rs, rung0_param_check.rs
F:\rust\wang2003\ <- Rung 0 learning project (plain-variable version)
F:\rust\POEL_2024-main\ <- reference Fortran code (Wang's own, compiled & run only)

## Slide 28
PART 4 · CODE WALKTHROUGH
lib.rs — Crate Root
📁 F:\rust\poroelastic_solver\src\lib.rs
pub mod coupling; pub mod diffusion; pub mod elasticity;
pub mod field; pub mod grid; pub mod linalg;
pub mod param; pub mod source;
pub use coupling::{SimState, SolverTolerances, StepReport};
pub use field::{Field3D, VectorField3D};
pub use grid::Grid3D;
pub use param::PoroLayer;
pub use source::InjectionWell;
Declares every module (pub mod) so the compiler includes them in the crate.
Re-exports (pub use) the main types so callers can write poroelastic_solver::SimState instead of poroelastic_solver::coupling::SimState.
The doc comment at the top of the file states the governing equations -- the crate's 'why' in one place.

## Slide 29
PART 4 · CODE WALKTHROUGH
grid.rs + field.rs — Grid and Data Storage
📁 F:\rust\poroelastic_solver\src\grid.rs and src\field.rs
pub struct Grid3D { pub nx: usize, ny: usize, nz: usize, dx: f64, dy: f64, dz: f64 }
impl Grid3D {
pub fn idx(&self, i,j,k) -> usize { i + self.nx*(j + self.ny*k) } // x-fastest flat index
pub fn coords(&self, i,j,k) -> (f64,f64,f64) { (i as f64*dx, j as f64*dy, k as f64*dz) }
}
pub struct Field3D { pub data: Vec<f64> } // one scalar per grid node
pub struct VectorField3D { pub ux: Field3D, uy: Field3D, uz: Field3D }
idx(i,j,k) maps 3D node coordinates to a position in a flat Vec<f64> -- x varies fastest, matching how the data is laid out in memory (cache-friendly for the i-loops).
VectorField3D::to_flat()/from_flat() pack the 3 displacement components into one long vector [ux|uy|uz] so the generic linear solvers (which only know about flat Vec<f64>) can be reused for both scalar (pressure) and vector (displacement) unknowns.

## Slide 30
PART 4 · CODE WALKTHROUGH
param.rs — The 5-Parameter Conversion
📁 F:\rust\poroelastic_solver\src\param.rs
pub struct PoroLayer { pub g: f64, nu: f64, nu_u: f64, b: f64, d: f64 }
impl PoroLayer {
pub fn lambda(&self) -> f64 { 2.0*self.nu*self.g / (1.0-2.0*self.nu) }
pub fn alpha(&self) -> f64 { 3.0*(nu_u-nu) / ((1.0-2.0*nu)*(1.0+nu_u)*b) }
pub fn inv_q(&self) -> f64 { /* Eq. 5 */ }
pub fn chi(&self) -> f64 { /* Eq. 6, uses d */ }
pub fn k_dr(&self) -> f64 { self.lambda() + 2.0*self.g/3.0 } // drained bulk modulus
}
Every method is a direct, one-line translation of a Wang & Kumpel (2003) equation number (comments cite them).
k_dr() was added later specifically to support the fixed-stress split's beta = alpha^2/K_dr stabilization term.
This is literally the same code as Rung 0 (wang2003/src/main.rs), just wrapped in a struct so multiple layers/scenarios can each carry their own set of parameters.

## Slide 31
PART 4 · CODE WALKTHROUGH
linalg.rs — Matrix-Free Linear Solvers
📁 F:\rust\poroelastic_solver\src\linalg.rs
pub fn conjugate_gradient<F: Fn(&[f64])->Vec<f64>>(apply_a: F, b: &[f64], x0: Vec<f64>, ...)
-> (Vec<f64>, usize) {
// standard CG: r = b - A*x; p = r; loop { alpha = rs/(p.Ap); x += alpha*p; ... }
}
pub fn bicgstab<F: Fn(&[f64])->Vec<f64>>(apply_a: F, b: &[f64], x0: Vec<f64>, ...)
-> (Vec<f64>, usize) { /* stabilized bi-conjugate gradients */ }
'Matrix-free' means apply_a is a closure that computes A*x directly via the stencil -- the matrix A is never assembled or stored, which is essential since A would be enormous (3N x 3N for elasticity, N = number of grid nodes).
CG requires the operator to be symmetric positive-definite; it is used only for the diffusion equation, where that's provably true.
BiCGSTAB tolerates non-symmetric operators; it is used for elasticity, where the free-surface ghost-node stencil isn't guaranteed to stay exactly symmetric.

## Slide 32
PART 4 · CODE WALKTHROUGH
elasticity.rs (1/2) — Ghost Nodes & Boundary Masks
📁 F:\rust\poroelastic_solver\src\elasticity.rs
fn is_fixed(grid, i, j, k) -> bool {
i==0 || i==nx-1 || j==0 || j==ny-1 || k==nz-1 // far-field: pinned to zero
}
fn ghost_uz(ux, uy, uz, grid, lambda, g, i, j) -> f64 {
if edge_of_domain { return 0.0; } // lateral edges: fixed wins
let dux_dx = /* central diff at k=0 */;
let duy_dy = /* central diff at k=0 */;
uz(i,j,1) + 2.0*dz*(lambda/(lambda+2.0*g))*(dux_dx + duy_dy) // Eq. from Part 2
}
is_fixed marks the far-field boundary nodes (sides + bottom) whose displacement is pinned to zero.
ghost_ux / ghost_uy / ghost_uz compute the 'value above the surface' needed by the k=0 stencil, from the traction-free relations derived in Part 2.

## Slide 33
PART 4 · CODE WALKTHROUGH
elasticity.rs (2/2) — The Stencil, Solve, Divergence
📁 F:\rust\poroelastic_solver\src\elasticity.rs
pub fn apply_elastic_operator(u_flat, grid, g, lambda) -> Vec<f64> {
for each node (i,j,k):
if is_fixed(i,j,k) { output = input; continue } // identity row
compute 9 second derivatives + 6 cross derivatives (ghosts at k=0)
Lx = (lambda+2G)*d2ux_dx2 + G*d2ux_dy2 + ... + (lambda+G)*d2uz_dxdz
(Ly, Lz analogous)
}
pub fn solve_elasticity(rhs, grid, g, lambda, x0, tol, max_iter) -> (VectorField3D, usize)
pub fn divergence(u, grid, lambda, g) -> Field3D // needed as a source for pressure eqn
apply_elastic_operator IS the matrix A from 'A*x=b', applied one grid node at a time -- this is what bicgstab calls every iteration.
divergence() reuses the exact same free-surface ghost formula so the mechanics and the pressure-equation source term stay numerically consistent.

## Slide 34
PART 4 · CODE WALKTHROUGH
diffusion.rs — Pressure Solve, With Stabilization
📁 F:\rust\poroelastic_solver\src\diffusion.rs
pub fn apply_diffusion_operator(p, grid, chi, coeff) -> Vec<f64> {
for each node: if k==0 { output = p (Dirichlet) }
else { output = coeff*p - chi*Laplacian(p) } // 7-point stencil, Neumann elsewhere
}
pub fn solve_diffusion(p_n, p_iter, beta, source, grid, chi, inv_q, dt, ...) -> (Field3D, usize) {
coeff = (inv_q + beta) / dt;
b[idx] = source + (inv_q/dt)*p_n[idx] + (beta/dt)*p_iter[idx]; // fixed-stress RHS
conjugate_gradient(|v| apply_diffusion_operator(v, ...), &b, ...)
}
beta=0.0 and p_iter=p_n recovers the plain (unstabilized) equation -- the fixed-stress version is a strict generalization, not a rewrite.

## Slide 35
PART 4 · CODE WALKTHROUGH
coupling.rs (1/2) — State and the Pressure-Gradient Source
📁 F:\rust\poroelastic_solver\src\coupling.rs
pub struct SimState { pub u: VectorField3D, pub p: Field3D }
pub struct SolverTolerances { picard_tol, picard_max_iter, cg_tol, cg_max_iter }
fn alpha_grad_p(p, grid, alpha) -> VectorField3D {
// alpha*grad(p), the RHS source for the elasticity solve;
// dp/dz at k=0 uses the odd-reflection ghost p(-1) = -p(1), since p=0 there exactly
}
SimState bundles the two coupled unknowns (displacement, pressure) that get updated together every time step.
alpha_grad_p turns the pressure field into the vector 'body force' that drives the elasticity solve -- it's the alpha*grad(p) term on the right-hand side of Eq. 1.

## Slide 36
PART 4 · CODE WALKTHROUGH
coupling.rs (2/2) — The Fixed-Stress Time Step
📁 F:\rust\poroelastic_solver\src\coupling.rs :: step()
pub fn step(state, grid, params, q_field, dt, tol) -> StepReport {
let beta = alpha*alpha / params.k_dr();
for it in 0..max_iter {
source = q - alpha*(div_u_iter - div_u_n)/dt; // flow step first
p_new = solve_diffusion(p_n, p_iter, beta, source, ...);
rhs = alpha_grad_p(p_new, ...); // then mechanics
u_new = solve_elasticity(rhs, ..., u_current, ...);
if |p_new - p_iter| < tol { break }
}
}
This IS the fixed-stress split algorithm from Part 2, translated line for line into code.

## Slide 37
PART 4 · CODE WALKTHROUGH
source.rs — The Injection Well
📁 F:\rust\poroelastic_solver\src\source.rs
pub struct InjectionWell { x0, y0, z0, sigma, schedule: Vec<(f64,f64)> }
pub fn source_field(&self, grid, t) -> Field3D {
let rate = self.rate_at(t); // look up schedule for this time
// w(x) = exp(-r^2 / (2*sigma^2)) / normalization -- a 3D Gaussian
// renormalize numerically so sum(w)*cell_volume == 1, then scale by rate
}
A true mathematical point source (Dirac delta) can't be represented on a finite grid -- it would need infinite pressure in a single cell.
Solution: smear the injection over a small Gaussian blob (sigma ~ 1-2 grid cells) that still integrates to exactly the correct total volume.
schedule is a list of (time, rate) pairs -- supports step changes, shut-ins, or any piecewise-constant history.

## Slide 38
PART 4 · CODE WALKTHROUGH
main.rs — The Example Driver
📁 F:\rust\poroelastic_solver\src\main.rs
let params = PoroLayer { g: 2.0e10, nu: 0.25, nu_u: 0.30, b: 0.6, d: 1.5 };
let grid = Grid3D::new(41, 41, 41, 150.0, 150.0, 150.0); // 6 km cube
let well = InjectionWell { x0:3000.0, y0:3000.0, z0:3000.0, sigma:1.5*dx,
schedule: vec![(0.0, 0.005)] }; // 0.005 m^3/s
for step_i in 0..60 { // 60 daily steps
let report = step(&mut state, &grid, &params, &q_field, dt, &tol);
// write CSV row: pressure at well, uplift at surface, picard_iters
}
write_vtk("final_field.vtk", &grid, &state) // full 3D field, open in ParaView
Run with: cargo run --release -> writes injection_timeseries.csv and final_field.vtk

## Slide 39
PART 4 · CODE WALKTHROUGH
tests/ — The Two Automated Checks
📁 F:\rust\poroelastic_solver\tests\elasticity_mms.rs, diffusion_point_source.rs
// elasticity_mms.rs
let u = quadratic_polynomial(x,y,z); // e.g. ux = x^2 + 2xy + 3xz, ...
assert!( (apply_elastic_operator(u,...) - analytic_value).abs() < 1e-8 );
// diffusion_point_source.rs
let p_num = solve_diffusion(...) /* 40 backward-Euler steps */;
let p_ana = analytical_carslaw_jaeger_formula(r, t);
assert!( (p_num - p_ana).abs() / p_ana < 0.2 );
Run with: cargo test --release (both currently pass)

## Slide 40
PART 4 · CODE WALKTHROUGH
examples/wk2003_comparison.rs — The Cross-Check
📁 F:\rust\poroelastic_solver\examples\wk2003_comparison.rs
let params = PoroLayer { g: 0.4e9, nu: 0.2, nu_u: 0.4, b: 0.75, d: 1.0 }; // W&K's own numbers
let grid = Grid3D::new(49, 49, 43, 5.0, 5.0, 5.0); // 240m x 240m x 215m
let well = InjectionWell { x0:120.0, y0:120.0, z0:60.0, ..., schedule: vec![(0.0, 32.0/3600.0)] };
for step_i in 0..80 { // dt=100s, 8000s total
step(&mut state, &grid, &params, &q_field, dt, &tol);
// write p at r=40m for z = 5, 15, 45, 75 m -> rust_solver_wk2003.csv
}
Run with: cargo run --release --example wk2003_comparison
Output was compared against POEL2024's wk2003_pp.dat -- this produced the headline validation result.

## Slide 41
PART 5
Results & Talking Points
The final numbers, how to explain them simply, and where to find everything.

## Slide 42
PART 5 · RESULTS
Final Validation Numbers
Check | What it proves | Result
MMS test | Elasticity stencil math is exact | < 1e-8 relative error
Analytical diffusion | Diffusion module matches theory | 0.2-2.5% error
POEL reproduction | We can reproduce the paper's own tool | Matches Fig. 2 shape + Noordbergum effect
Rust vs. POEL (fixed-stress) | Our full coupled code is correct | 0.2-2.5% (early time), 11-17% (late, explained)
Every number above is reproducible: re-run cargo test, cargo run --example wk2003_comparison, and the plotting scripts in poroelastic_solver/validation_plots.

## Slide 43
PART 5 · RESULTS
Explaining the Fixed-Stress Split Simply
If your professor asks "why did you need this fix?":
"Solving pressure and deformation by just alternating between them works fine most of the time -- but for very soft, strongly-coupled rock, that back-and-forth can amplify errors instead of shrinking them."
"The fix holds the total stress fixed while solving for pressure, which is a mathematically provable way to guarantee the iteration always converges, no matter how strong the coupling."
"I found this the hard way: my code diverged on the paper's own worked example, traced it to the coupling scheme (not the physics), and fixed it with a well-known technique from the poromechanics literature (Kim, Tchelepi & Juanes 2011)."

## Slide 44
PART 5 · RESULTS
Known Limitations & Future Work
Single homogeneous layer, not the paper's layered Earth model -- would need a fundamentally different (layered propagator) numerical method, or a much more complex FD grid with per-layer properties.
Finite domain approximates an infinite half-space -- must stay large relative to sqrt(D*t_max); the late-time drift in the validation traces directly to this.
No Coulomb-stress or seismicity-rate modeling (Eq. 3 of the PNAS paper) -- this project solves only the poroelastic PDE system, not the earthquake-nucleation model built on top of it.
Possible next step: implement a proper Laplace-Hankel-propagator solver (like POEL) for direct, non-approximate comparison to layered/axisymmetric cases.

## Slide 45
PART 5 · RESULTS
Quick Reference: Where Everything Lives
Main crate: F:\rust\poroelastic_solver\
Rung 0 project: F:\rust\wang2003\
Reference code: F:\rust\POEL_2024-main\ (compiled with gfortran via MSYS2)
Plots & report: F:\rust\poroelastic_solver\validation_plots\ (VALIDATION_SUMMARY.md)
PNAS paper: C:\Users\Asus\Downloads\PNAS_2019.pdf
Wang & Kumpel (2003): C:\Users\Asus\Downloads\wang2003.pdf
Build & test: cargo build --release | cargo test --release
Run demo: cargo run --release (writes injection_timeseries.csv, final_field.vtk)